CC Publication No. MNG-500                             V.2 (4/77)
















                System Manager's Guide to TECO-11

          (Describing Version 17 of TECO-11 for RSTS/E)


                            Version 2

                            April 1977




                     TECO-11 was written by:

      Russell Hamm, Hank Maurer, Bob Hartman, Mark Bramhall,
         Anton Chernoff, Richard Lary, and Mario DeNobili




                      Authors of this Guide:

                          G. Paul Koning
                       Lawrence University
                         Computer Center

                          James S. Evans
                       Lawrence University
                     Department of Chemistry







            Prepared and published by the staff of the
                       Lawrence University
                         Computer Center
                    Appleton, Wisconsin 54911

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 2



This  Guide  has  been  prepared  for  members  of  the   Lawrence
University  community.   It provides information on installing and
managing TECO-11 as an  alternate  run-time  system  under  RSTS/E
(V06B-02)  on  the  PDP-11/45.  System  managers will also wish to
refer  to  the  TECO  Introductory  Manual  (CC  Publication   No.                ____  ____________  ______
EDU-510)  and/or  the TECO-11 Reference Manual (CC Publication No.                      _______ _________ ______
EDU-500).  Readers'   suggestions   for   improvements   to   this
documentation  will  be  welcomed  by the authors and the Computer
Center.


Copyright  (C)  1975,  1976,  1977  by  Lawrence   University   of
Wisconsin.   General  permission  to  copy  or modify, but not for
profit, all or part of this Guide is hereby granted, provided that
Lawrence's copyright notice is given, and reference is made to the
fact that reproduction privileges were granted  by  permission  of
Lawrence University of Wisconsin.

Although every effort has been made to insure that this  Guide  is
accurate  and  that TECO-11 is free of errors, neither the authors
of TECO-11  or  of  this  publication,  Lawrence  University,  its
funding  sources,  nor  Digital  Equipment  Corporation  make  any
warranty, expressed or implied, with respect to the correctness of
the  information  contained in this publication or the functioning
of TECO-11.

The following are trademarks  of  Digital  Equipment  Corporation,
Maynard, Massachusetts:  DEC, DECtape, Digital, PDP, RSTS/E.


This publication was edited on a PDP-11/45 at Lawrence  University
using TECO-11 under RSTS/E (V06A-02, V06B-02). Layout was effected
under RSTS/E using Lawrence's RUNOFF text formatting program.  The
copy  masters  were  obtained on an IBM 360/44 at The Institute of
Paper Chemistry, Appleton, under OS/PCP using  Lawrence's  program
READRSTS  to drive an IBM 1403 printer with an IBM TN print chain.

Portions of the computing resources  available  at  Lawrence  were
purchased  with  grants  from the National Science Foundation, the
National Endowment  for  the  Humanities,  the  Andrew  W.  Mellon
Foundation,  the  Lilly Endowment, the American Council of Learned
Societies, and the United States Steel Corporation.  Their support
is gratefully acknowledged.

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 3



                        TABLE OF CONTENTS                        _________________


Section                                                       Page_______                                                       ____

1  What is TECO-11?                                              3
2  Contents of the TECO-11 distribution medium                   4
3  Instructions for installing TECO-11 under RSTS/E, V06B-02     4
4  Using TECO-11 under RSTS/E, V06B-02                           7
5  Optional tailoring for installation-dependent characteristics 7
6  Feasibility of installing TECO-11 under older RSTS/E releases 9




1.  What is TECO-11?    ________________

TECO-11 is an extremely sophisticated  and  fast,  yet  relatively
easy to learn, character-oriented text editor.  That is, it treats
a text file as a sequence of characters;   however,  it  also  has
numerous  line-oriented  editing  commands.   TECO-11  can perform
character-string   searches,   replacements,    insertions,    and
deletions;  moreover, it has advanced features such as repetitive,
conditional, and macro commands.

TECO-11, as implemented under RSTS/E, is  an  "alternate  run-time
system";  as far as the RSTS/E monitor is concerned, TECO-11 has a
status similar to that of the  BASIC-PLUS  run-time  system.   The
TECO-11  run-time  system  consists  of 4K of read-only, reentrant
code that is shared by all users.  Unlike BASIC-PLUS, however, the
TECO-11  run-time system need not be resident in memory when it is
not in use.  Users gain access to TECO-11 via a  brief  BASIC-PLUS
program that handles CCL commands and then requests RSTS/E to load
the run-time system if it is not already resident.

TECO-11 uses only features of RSTS/E  that  are  fully  supported,
integral  parts  of the system;  it does not in any way compromise
system reliability or security  any  more  than  a  non-privileged
BASIC-PLUS   program   would.    In   particular,  TECO-11  relies
completely upon the RSTS/E monitor's file processor  to  grant  or
deny  read/write  access  to  input  and  output files, based upon
protection codes and the user's privileged/non-privileged  status.

TECO-11 has been checked out carefully and has  been  used  for  a
long time at various installations, including Lawrence University.
Nevertheless, neither Lawrence nor the authors of TECO-11  can  or
will make any warranties with respect to the correctness or proper
functioning of the program, nor should they be held liable for any
damages  or  losses of user files resulting directly or indirectly
from the use of TECO-11.

The remaining sections of this Guide discuss the contents  of  the
TECO-11  distribution  medium, the installation procedure, and the
use of TECO-11 under RSTS/E.

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 4



2.  Contents of the TECO-11 distribution medium    ___________________________________________

The RSTS/E distribution medium (magtape with DOS labels,  DECtape,
or RK05 disk) contains the following files:

TECO6B.RTS    A copy of the code (in  SILUS  format)  constituting
              the TECO-11 run-time system for RSTS/E, V06B-02.

TECO6A.RTS    A copy of  the  core  image  code  constituting  the
              TECO-11 run-time system for RSTS/E, V06A-02.

TECO  .LDA    A dummy file  required  in  order  to  activate  the
              TECO-11 run-time system for each new user.

TECO6B.BAS    The BASIC-PLUS program used to handle  CCL  commands
              and  initiate  execution  of  the  TECO-11  run-time
              system for RSTS/E, V06B-02.

TECO6A.BAS    The BASIC-PLUS autoloader used to load and  initiate
              execution of the TECO-11 run-time system for RSTS/E,
              V06A-02.

DOCFIL.DOC    Sample formatted text (2 pages)  that  explains  and
              tests  the  retrieval  and printing procedures to be
              used  for  the  files  TECOMG.DOC,  TECOIM.DOC,  and
              TECORM.DOC,  which  contain  the  TECO-11 manuals in
              '.DOC' format.

TECOMG.DOC    The formatted text of CC Publication  No.   MNG-500,
              System Manager's Guide to TECO-11 (this publication,              ______ _________ _____ __ _______
              11 pages).

TECOIM.DOC    The formatted text of CC Publication  No.   EDU-510,
              TECO Introductory Manual (25 pages).              ____ ____________ ______

TECORM.DOC    The formatted text of CC Publication  No.   EDU-500,
              TECO-11 Reference Manual (2+84 pages).              _______ _________ ______

The '.DOC' files  describe  the  TECO-11  editor  for  the  system
manager,  for  beginners,  and  for  experienced users.  Copies of
these manuals  may  be  run  off  or  reproduced  as  needed  (see
copyright notice on the second page of each document).



3.  Instructions for installing TECO-11 under RSTS/E, V06B-02    _________________________________________________________

          Important: The instructions  in  this  section          _________
          and  in  section  5  below pertain only to the                                             ____
          installation  of  TECO-11  under  the  current
          release (V06B-02) of RSTS/E. Section 6 of this
          manual   discusses    the    feasibility    of
          implementing TECO-11 under earlier releases of
          RSTS/E.

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 5



TECO-11, version 17, can be  installed  while  timesharing  is  in
progress,  using  several  of Digital's utility programs and items
from the distribution medium.  Follow the instructions exactly  as
given  below.  Carriage return is denoted by <CR> and control-Z by
<CTRL/Z>. Header identifications  printed  by  standard  utilities
have been suppressed from the sample dialogs.

To install TECO-11, version 17, on  your  RSTS/E  system,  V6B-02,
proceed as follows:

a.  Log on to any privileged  account.   If  you  already  have  a                  __________
    run-time  system  called  'TECO', take steps to remove it with
    UTILTY and rename it.  Otherwise, the /UP switch in  step  'd'
    below will overwrite it.

b.  Assign a physical drive and  mount  the  distribution  medium,
    write-locked  if  possible  (RK05  disk pack must be logically
    mounted). Associate the logical name 'DIS' with  the  physical
    device  via  the command 'ASSIGN dev:DIS'. Proceed to step 'd'
    if the distribution medium is DECtape.

c.  If the distribution medium is magtape or RK05 disk,  find  the
    project-programmer  number  [m,n]  under  which  the files are
    stored and then define the symbol '@', which is used  in  step
    'd' below:

        RUN $PIP <CR>
        #DIS:/DI <CR>
        directory listing for [m,n]
        # <CTRL/Z>
        Ready
        ASSIGN [m,n] <CR>
        Ready

d.  The core image of the read-only code for the  run-time  system
    (TECO6B.RTS, in SILUS format) must be transferred into account
    [0,1] as a contiguous file.  The dummy file (TECO.LDA) must be               __________
    transferred  into  the  system library account and marked as a
    "compiled" program.  Follow this dialog:

        OPEN"SY0:TECO.RTS[0,1]/MO:16/SI:21"FOR OUTPUT ASFILE1%<CR>
        Ready
        RUN $PIP <CR>
        #SY0:TECO.RTS[0,1]/CO:T/UP=DIS:TECO6B.RTS@ <CR>
        #SY0:TECO.LDA$/CO:T/UP=DIS:TECO.LDA@/RW:NO <CR>
        #=SY0:TECO.LDA$<104>/RE <CR>
        # <CTRL/Z>
        Ready

e.  UTILTY is now used to mark the dummy file for TECO and to  add
    TECO  to  the  table  of  accessible  run-time systems for the
    current timesharing session.  Decide  upon  the  maximum  text
    buffer area in K words of memory, denoted by 'yy' below, to be
    allowed for any user of TECO-11 during the current timesharing
    session.   The quantity 'yy' must be less than or equal to 28;

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 6



    it must also be less than or equal to  (SWAPMAX  -  4).  While
    TECO-11  will  operate  with  as little as 2K per user, a more
    realistic minimum would be 4K. Follow this dialog:

        RUN $UTILTY <CR>
        #NAME TECO=SY0:TECO.LDA$ <CR>
        #ADD TECO/MAX:yy <CR>
        # <CTRL/Z>
        Ready

    The naming operation is permanent, provided that  TECO.LDA  is
    not  recopied  by  utility  programs  (e.g.  PIP) which do not
    preserve the run-time  system  identification  in  the  file's
    directory  entry.   In  contrast,  to  insure  that TECO-11 is
    accessible  during  every  timesharing  session,  it  will  be
    necessary  to  edit  the  START.CTL  and  CRASH.CTL  files  by
    insertion of a command to UTILTY of the form:

          FORCE KB0: ADD TECO/MAX:yy

    Refer to the RSTS/E  System  Manager's  Guide  for  additional                 ______  ______  _________  _____
    information  about  control  of  run-time  systems.   With the
    autoloader program supplied in this  distribution,  it  should
    not  be  necessary  to  use  the  LOAD  and UNLOAD commands in
    UTILTY.

f.  The autoloader program should be compiled, but it  should  not                                                               ___
    be  marked as a privileged program.  The protection code of 40
    specified in the following dialog is converted to  104  during
    the compilation process, and will grant execute-only access to
    all users:

        OLD DIS:TECO6B@ <CR>
        Ready
        COMPILE SY0:TECO$<40> <CR>
        Ready

g.  TECO-11 is now installed on your system.  Any user may  access
    it  with  the  command 'RUN $TECO'. If you wish to have RSTS/E
    respond to the CCL commands 'TECO' and "MAKE', as described in
    the  TECO-11  Reference Manual, those commands must be defined         _______  _________ ______
    for the current timesharing session using UTILTY:

        RUN $UTILTY <CR>
        #CCL TECO-=$TECO.BAC;30000 <CR>
        #CCL MAKE-=$TECO.BAC;30000 <CR>
        # <CTRL/Z>

    To make these features permanent, the START.CTL and  CRASH.CTL
    files should be modified appropriately.

h.  Follow the instructions  in  the  file  DOCFIL.DOC  to  obtain
    printed  copies  of  the  manuals.   Dismount the distribution
    medium and store it safely.

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 7



4.  Using TECO-11 under RSTS/E, V06B-02    ___________________________________

To use TECO-11 after it is installed, use the command 'RUN $TECO'.
TECO-11  will  respond  with  "*"  to indicate that it is ready to
accept a command.  Refer  to  the  TECO  Introductory  Manual  (CC                                   ____  ____________  ______
Publication  No.   EDU-510)  for  a  useful subset of commands and
elementary illustrations of text editing with TECO-11.

If you have implemented the TECO and MAKE  commands  in  your  CCL
table (see 3.g above), you will also want to know that:

a.  The TECO command enters TECO-11 and opens the  file  named  in
    the  TECO  command for editing (effect of the EB command); the
    first page of the file is read into the buffer (effect of  the
    Y command).

b.  The MAKE command, on the other hand, opens the file  named  in
    the command for output (effect of the EW command).

c.  When given without arguments, the TECO and MAKE  commands  are
    equivalent to 'RUN $TECO'.

The above information and full instructions on using  TECO-11  are
contained in the TECO Reference Manual (CC Publication EDU-500).                 ____ _________ ______

Neither the autoloader program  ($TECO.BAC)  nor  the  dummy  file
($TECO.LDA)  can convey special privileges to nonprivileged users,
because the TECO-11 run-time system drops any  special  privileges
irreversibly   during   its  initialization  for  each  new  user.
Thereafter, TECO-11 does  not  affect  file  security,  since  the
RSTS/E monitor checks file protection codes and project-programmer
numbers.  The ER (edit read)  and  EW  (edit  write)  commands  in
TECO-11   are   functionally  equivalent,  so  far  as  RSTS/E  is
concerned, to the OPEN FOR INPUT and OPEN FOR OUTPUT statements in
BASIC-PLUS.




5.  Optional Tailoring for installation-dependent characteristics    _____________________________________________________________

          Important: The  information  in  this  section          _________
          pertains   only  to  TECO-11  for  V06B-02  of                     ____
          RSTS/E.  The  modifications  described   below
          should be attempted only if there is a genuine
          need for them.  Because of its  special  SILUS
          format,  TECO6B.RTS  can be modified only with                                               ____
          the PATCH option of INIT.SYS;  the file  would
          be    destroyed    by    PATCH.SAV   or   ODT.
          Consequently,   the    person    making    the
          alterations should be thoroughly familiar with
          the PATCH option.

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 8



Optional patch 17.1 for TECO.RTS (for RSTS/E V06B-02):

The distributed version of TECO-11 for RSTS/E  V06B-02  recognizes
the  standard library accounts associated with certain symbols ($,
!, %, &). If the system manager specified nonstandard  values  for
these  symbols  during SYSGEN for his RSTS/E system, this optional
patch may be performed to modify the internal file name scanner in
TECO.RTS accordingly.

Terminate the current timesharing session to bring  INIT.SYS  into
operation.   The  numbers  'm'  and 'n' in the procedure described
below refer to a new account designation  [m,n]  for  one  of  the
special  library accounts;  typing a line feed will retain the old
value and inspect the next one.  Proceed as follows.


Option: PATCH
File to patch? TECO.RTS
Base address? PN
Offset address? 0
 Base   Offset  Old       New?
??????  000000  000402  ? m*400+n <CR>  {<LF> retains [1,2]=$}
??????  000002  000403  ? m*400+n <CR>  {<LF> retains [1,3]=!}
??????  000004  000404  ? m*400+n <CR>  {<LF> retains [1,4]=%}
??????  000006  000405  ? m*400+n <CR>  {<LF> retains [1,5]=&}
??????  000010  ??????  ? <CTRL/C>


Optional patch 17.2 for TECO.RTS (for RSTS/E V06B-02):

The distributed version of TECO-11 for RSTS/E  V06B-02  recognizes
the  "exit  and  go" extensions described in section 3.10.3 of the
TECO-11 Reference Manual (CC Publication  No.   EDU-500).  The  EG_______ _________ ______
command  compares  the extension of the edited output file against
those in its internal recognition table.  If  a  match  is  found,
TECO-11  requests  RSTS/E  to search in the system library account
[1,2] for the first corresponding utility program in compiled form              _____
whose  extension matches one of the active run-time systems in the
monitor's tables.  The search proceeds in the order of the various
run-time systems in the monitor's linked list.

The recognition table initially consists of five entries, followed
by  a  zero  word, followed by slots for three additional entries.
Each entry consists of four words:  the extension for EG to  match
against  the  edited  file's extension (RAD50), the account number
where the utility program resides (m*400+n  for  [m,n]),  and  the
name  of  the  utility  program  (two  RAD50 words). The following
optional patch may be performed to change, add, or delete  entries
in the recognition table used by the EG command.

Terminate the current timesharing session to bring  INIT.SYS  into
operation.   Let  the  entry  to  be  changed  be  denoted  by 'e'
(e=0,1,2,3,4,5,6,7). Also be sure that a  zero  word  follows  the
last  valid entry 'z' in the table (i.e. the word at offset = 10*z
must be zero). Decide on the extension to be recognized (ext)  and

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500     Page 9



the  corresponding  utility  program  name  (filnam).  Proceed  as
follows.

Option: PATCH
File to patch? TECO.RTS
Base address? EGFILS
Offset address? 10*e
 Base   Offset  Old       New?
??????  ?????0  ??????  ? %ext <CR>    {extension to match}
??????  ?????2  ??????  ? m*400+n <CR> {account [m,n]}
??????  ?????4  ??????  ? %fil <CR>    {3 characters of filename}
??????  ?????6  ??????  ? %nam <CR>    {3 characters of filename}
??????  ?????0  ??????  ? <CTRL/C>



6.  Feasibility of installing TECO-11 under older RSTS/E releases    _____________________________________________________________

          Important: The information in this section  is          _________
          completely    irrelevant   for   installations          __________    __________
          running  the  current  release  (V06B-02)   of
          RSTS/E.  This section is based on considerable
          experience with TECO-11 under RSTS/E  releases
          V05B-24  and  V06A-02  at Lawrence University,
          but no assurance can  be  given  that  TECO-11
          will function properly at other installations.

The  distribution  medium  includes  two  files,  TECO6A.RTS   and
TECO6A.BAS,  which  have  until  recently  been  in  operation  at
Lawrence University under RSTS/E,  V06A-02.  Special  instructions
for installing them are given below.

Because of changes in the techniques used by TECO-11 and by RSTS/E
to  assure  maximum  file  security, neither 'TECO6A' nor 'TECO6B'
will  run  under  RSTS/E  versions  V5B  or  V5C.  There  is  some
possibility  that  special  versions  could  be  prepared for such
retrofits,  but  Lawrence  University  would  have  to  charge   a
consultant's fee in addition to recovering all of its direct costs
in such preparation.  Inquiries should be  directed  to  Professor
Evans at the address on the first page of this document.

It is utterly impossible to run TECO-11 under versions  of  RSTS/E
prior  to  V05B-24,  since  earlier  monitors  lacked  support for
alternate run-time systems.

Alternate run-time systems may not be  practicable  on  small-core
machines  because  each such run-time system under RSTS/E versions
prior to V06B-02 must remain effectively locked in memory so  long
as  its active user count is nonzero.  There must be enough memory
(in K units) to accommodate the sum of:

    4K, for the TECO-11 run-time system
and___
    SWPMAX, for the largest permissible user core image (i.e.  for
    privileged users and privileged programs)

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500    Page 10



and___
    ??,  space  for  permanently loaded run-time systems, or other
    autoloading run-time systems that the system manager allows to
    run simultaneously with TECO-11

Thus it may be necessary to lower SWPMAX at installations  cramped
for  memory,  if  the  message  "No  room  for  user on device" is
obtained at step 3.g below.

To attempt installation  of  TECO-11,  Version  17,  on  a  RSTS/E
system, V06A-02, proceed as follows:

a.  Log on to any privileged  account.   If  you  already  have  a                  __________
    run-time  system  called  'TECO', take steps to remove it with
    UTILTY and rename it.  Otherwise, the /UP switch in  step  'd'
    below will overwrite it.

b.  Assign a physical drive and  mount  the  distribution  medium,
    write-locked  if  possible  (RK05  disk pack must be logically
    mounted). Associate the logical name 'DIS' with  the  physical
    device  via  the command 'ASSIGN dev:DIS'. Proceed to step 'd'
    if the distribution medium is DECtape.

c.  If the distribution medium is magtape or RK05 disk,  find  the
    project-programmer number under which the files are stored and
    define the symbol '@, which is used in step 'd' below'.

d.  The core image of the read-only code for the  run-time  system
    (TECO6A.RTS)  must be transferred into account [0,1] as a file
    consisting of a  single  16-block  cluster.   The  dummy  file
    (TECO.LDA) must be transferred into the system library account
    and marked as a "compiled" program.  Follow this dialog:

        RUN $PIP <CR>
        #SY0:TECO.RTS[0,1]<DIS:TECO6A.RTS@/CO:T/CL:16/UP <CR>
        #SY0:TECO.LDA$<DIS:TECO.LDA@/CO:T/UP/RW:NO <CR>
        #=SY0:TECO.LDA$<104>/RE <CR>
        # <CTRL/Z>
        Ready

e.  UTILTY is now used to mark the dummy file for TECO and to  add
    TECO  to  the  table  of  accessible  run-time systems for the
    current timesharing session.  Follow this dialog:

        RUN $UTILTY <CR>
        ? NAME TECO=SY0:TECO.LDA$ <CR>
        ? ADD TECO <CR>
        ? EXIT <CR>
        Ready

    Note: To  insure  that  TECO-11  is  accessible  during  every    ____
    timesharing   session,  it  will  be  necessary  to  edit  the
    START.CTL and CRASH.CTL files by insertion  of  a  command  to
    UTILTY of the form:

                    
System Manager's Guide to TECO-11 - CC Pub. No. MNG-500    Page 11



        FORCE KB1: ADD TECO

    The  RSTS/E  System  Manager's  Guide  discusses  control   of         ______  ______  _________  _____
    run-time  systems.   With  the  autoloader program supplied in
    this distribution, it is not necessary to  use  the  LOAD  and
    UNLOAD commands in UTILTY.

f.  Compile the autoloader program and mark  it  as  a  privileged
    program:

        OLD DIS:TECO6A@ <CR>
        COMPILE SY0:TECO$ <CR>
        Ready
        NAME "TECO.BAC$" AS "TECO.BAC$<232>" <CR>
        Ready

    The autoloader program (TECO.BAC) has to run as  a  privileged
    program  in order to execute certain privileged SYS functions,
    but these special  privileges  are  dropped  as  soon  as  the
    TECO-11 run-time system has been entered.

g.  TECO-11 is now installed on your system.  Any user may  access
    it with the command 'RUN $TECO'.

    Note: TECO-11 will not load unless the loading process  leaves    ____
    free  a contiguous block of memory large enough to accommodate
    the SWPMAX which the system manager declared for  the  current
    timesharing session.

    If you wish to have RSTS/E respond to the CCL commands  'TECO'
    and  'MAKE',  as  described  in  the TECO-11 Reference Manual,                                         _______ _________ ______
    those commands must be entered into the table of CCL  commands
    at SYSGEN time for RSTS/E (V6A-02). The procedure is explained
    in the RSTS/E System Generation Manual.           ______ ______ __________ ______

h.  Follow the instructions  in  the  file  DOCFIL.DOC  to  obtain
    printed  copies  of  the  manuals.   Dismount the distribution
    medium and store it safely.